## Slide 1
CNC machinery
1. Understanding CNC machines

## Slide 2
2
CNC machinery
1. Understanding CNC machines

## Slide 3: Learning outcomes
You will be able to:
Identify and describe common forms of CNC machining.
Image © This Is Engineering
3
1. Understanding CNC machines
Identify some advantages and disadvantages of using CNC.
Know what CAD, CAM and CNC stand for and be able to define each.

## Slide 4: What does CNC mean?
CNC machines are used in a wide range of engineering and manufacturing environments.
Discuss the two images on the left. What is the key difference that helps to explain what CNC means?
Can you expand and define the following terms: CAD, CAM and CNC?
4
1. Understanding CNC machines
Image © This Is Engineering

## Slide 5: What does CNC mean? Answers
CAD: computer-aided design
CAD uses computer software to create digital designs for objects or components.
CNC is a form of automation and therefore requires a control system with inputs, processing, outputs and feedback.
Describe what the input, control, output and feedback elements a CNC machine might be (their type) or do (their function).
5
1. Understanding CNC machines
CAM: computer-aided manufacturing
CAM uses computer software to generate tool paths and instructions to create these designs. (Also known as computer-aided modelling.)
CNC: computer numerical control
CNC codes drive toolhead and machine movements to machine materials and form these designs.
Design code
Tool path code
Image © This Is Engineering & rawpixel.com on Freepik

## Slide 6: The CNC control process
CNC is an example of automation and so it is helpful to think of a CNC machine as a control system:
This control system is common to all types of CNC machines.
Can you name or describe some different types of CNC machine?
A display monitor shows the program and other control or operating data​.
Computer or microprocessor follows input instructions, adjusts in response to feedback.
Finished workpiece
Position and speed transducers continuously monitor the tool head.
Input
Output
Feedback
Input device
Machine control unit
Machine drive system
Sensors
Amplifier circuits drive motors and ball lead screws that control the tool head.
1. Understanding CNC machines
6

## Slide 7: Common CNC machines
1. Understanding CNC machines
Discuss each type of machine:
What type of components can be produced?
What type of materials can be used?
7
Router
Simple cutting of softer materials, usually sheet material.
Milling
Detailed, precise cutting of hard materials in 3D.
Lathe
Cutting a cylinder of material as it spins on an axis.
Drilling
Drilling, reaming or tapping holes of different depths and diameters.
Laser or plasma cutting
Cutting that uses a laser or plasma to create a cut line and edge in sheet material.
Grinding
An abrasive wheel or cylinder produces a fine, accurate finish.

## Slide 8: Common CNC machines
These are all examples of subtractive manufacturing, where material is removed to create the finished part.
1. Understanding CNC machines
8
Router
Milling
Latahe
Drilling
Grinding
Laser or plasma cutting
Adding holes and screw threads to parts in almost any material, shaped using other CNC machines.
Cutting shaped parts from sheet metal such as flat components, lattice or grid parts, or certain small gears.
Cutting shaped parts from wood, plywood, MDF or laminated composites such as flat components, furniture parts.
Any 3D metal part such as engine blocks, structural parts, bevel, screw or worm gears, impellers.
Creating a fine finish on parts shaped using other CNC machines.
Cylindrical parts in metals or wood including furniture parts, axles, bolts, camshafts.

## Slide 9: Why is CNC used?
CNC machines, along with CAD/CAM packages, can represent a significant investment cost to buy and overhead cost to maintain. However, this can be offset by the reduced cost of hiring and training skilled labour to manually produce parts.
What broader advantages might motivate a company to invest in CNC?​
Are there any other disadvantages to investing in CNC that the company might need to consider?
9
1. Understanding CNC machines
Image © This Is Engineering

## Slide 10: Why is CNC used? Answers
Advantages | Disadvantages
Safer – operators are not exposed to material or cutting tools. Can run 24 hours a day, for higher productivity and large production volumes. Higher degree of control, for higher quality and consistency. Range of processes (drill, cutting, mill, threading, tapping etc.) creates flexibility. Reduces wastage – helps with overall production costs. More complex multi-axis machines can produce complex forms. Feedback systems indicate wear for planned maintenance and less unplanned downtime. | Operators need training, including in simple computer operation. May lead to workforce redundancies. Faults require highly skilled maintenance, usually contracted in. Faults may halt entire production line.
Use your answers to consider what advice you would give to a small local company that produces a range of bespoke designs. Are there reasons to use manual machining, or should they also invest in CNC?
10
1. Understanding CNC machines

## Slide 11: CNC in small-run settings
Manual machining still has many advantages for a small-run or bespoke engineering company:
Lower set up costs and overheads​.
Responsive: easier to make changes and experiment with ideas.​
Shorter turnaround time to set up machines.
Skilled operators understand machine limitations.
Ideal for simple components, low volume​.
However, even if producing small numbers of parts, these may need to be machined to exacting specifications, in which case customers may be willing to pay the increased cost for precision parts made using CNC.
These customers may include:
aerospace
research and development
scientific research
space exploration
other precision engineering companies who outsource work.
11
1. Understanding CNC machines
Image © This Is Engineering

## Slide 12: CNC in your engineering career
What parts or products are produced in the engineering or manufacturing sectors of interest to you?
What types of CNC machine will produce these?
A CNC operator is seen as a highly skilled job. What knowledge and skills do you think a CNC operator needs?
12
1. Understanding CNC machines
Image © This Is Engineering

## Slide 13: CNC in your engineering career – example
Sector | Part or product | CNC machines used | Knowledge and skills needed
Motorbike engineering | Brake levers | Mill – to shape Drill – create and tap holes Grinder – finish surface | Machine safety Personal safety and protection Machine operation Machine control (eg program loading) Material properties Required tolerances and quality level
13
1. Understanding CNC machines

## Slide 14: Learning outcomes
You will be able to:
Identify and describe common forms of CNC machining.
Image © This Is Engineering
14
1. Understanding CNC machines
Identify some advantages and disadvantages of using CNC.
Know what CAD, CAM and CNC stand for and be able to define each.