## Slide 1
Microcontroller systems 4. Pulse width modulation

## Slide 2: Practitioner guide 4. Pulse width modulation
2

## Slide 3: Introduction and overview
Resource name | Level | PPT slides + notes – practitioner | PPT slides - learner | Activity sheets | Film | Interactive
4. Pulse with modulation | 3 |  |  | 2 |  | 
These resources help practitioners to deliver the microcontroller systems components of engineering and manufacturing-related qualifications at levels 2 and 3.. They introduce the topic and stimulate learners to explore and reflect on key concepts and are designed to complement and enhance practitioners’ own lesson materials and schemes of work.
Resources summary
Prerequisites – it is recommended that learners complete 1. Mechatronic systems and control, 2. Sensors and signals and 3. Understanding control processes before starting this resource.
The Level 3 resources develop learners’ understanding of sensors and actuators before using a series of realistic but simple scenarios to provide an introduction to PLCs and PLC programming. We suggest that practitioners adapt the activities to suit the range of sensors, actuators and PLCs available in their place of learning or which relate to learners’ industrial placements. Practical extension suggestions enable learners to practise PLC programming using your preferred tool, software or simulator and to build a complete demonstration system.
Delivery
Delivery suggestions for practitioners, and suggested answers where appropriate, are in the presenter’s notes for each slide. The core activities in each resource provide around 60 mins learning time, though additional suggestions, including independent learning, can extend this time significantly.
Overarching theme/big questions
What is a mechatronics/automated system?
What is the role of programmable logic controllers (PLCs) in mechatronics?
Overview
The Level 2 resource provides a bridge between Level 2 and Level 3. It helps learners to understand the purpose and features of a mechatronic system, identify examples of mechatronic systems in a range of settings, describe in simple terms how the different components in a mechatronic system work together to control a process, and identify some differences between a microcontroller, PLC and microcomputer, suggesting suitable applications for each.
4. Pulse width modulation | Practitioner guide
3

## Slide 4: Learning outcomes and resource links
Level 3 resource 3
Pulse width modulation
Describe pulse width modulation (PWM).
Identify how PWM can control a range of devices including LEDs, DC motors and servo motors.
Make calculations to generate the right PWM signal to obtain desired results.
Full resource list available for the topic of Microcontroller systems:
1. Mechatronic systems and control (Level 2)
2. Sensors and actuators (Level 3)
3. Understanding control processes (Level 3)
4. Pulse width modulation (Level 3)
Links to other supported topics
Sustainability, Robotics, CNC machinery, Renewable energy, Electric machines.
4
4. Pulse width modulation | Practitioner guide

## Slide 5: Subject coverage
Microcontrollers and PLCs
Mechatronics
Sensors and actuators in automation and control
Programmable Logic Controllers (PLCs)
PLC programming
Applications of PLCs
Control system theory
Pulse width modulation
Including careers
How different engineering sectors use control and automation.
Maths
Using formulas
Percentages
Averages
Patterns and relationships
Communicating
Mathematical diagrams
5
4. Pulse with modulation | Practitioner guide

## Slide 6: 4. Pulse width modulation
6

## Slide 7: Learning outcomes
Identify how PWM can control a range of devices including LEDs, DC motors and servo motors.
Describe pulse width modulation (PWM).
You will be able to:
Make calculations to generate the right PWM signal to obtain desired results.
7
Image © This Is Engineering

## Slide 8: Microcontroller outputs
Discuss what output devices might operate each of these three functions?
How would the microcontroller need to change the state of each device?
What output signal might control these changes of state?
This CNC machine uses a microcontroller to operate the tool head rotation speed, vertical position and red/amber/green status indicator.
8

## Slide 9: Microcontroller outputs
9
The tool head might use a DC motor. The position might be changed by a servo; one or more LEDs might indicate the status of the machine.
The motor‘s speed will be controlled between a minimum and maximum level, appropriate to the tool and the material.
The servo’s position must be set so the tool rises and descends to the correct machining depth. The LED should change from green to amber and then red if there is a minor or major problem.
To produce these changes, the microcontroller could send a varying signal to the motor and servo, and an on-off signal for different LEDs.

## Slide 10: Control signal relationships
LED off/on
What kind of signal is being used in each case?
What does each axis represent in each chart?
What is the relationship between the signal and the state of each device?
DC motor speed
Servo motor position
10
The three charts show how a signal from the microcontroller can change the state of a status LED, DC motor speed and servo motor position.

## Slide 11: What is pulse width modulation?
Pulse width modulation (PWM) is a form of digital to analogue conversion (DAC).
PWM varies the time for which the output voltage is set high (the duty cycle) in a set frequency.
Output devices like DC motors interpret this as the average voltage during each period.
The bars in the diagram below show how the pulse widths in this signal vary. Each pulse is 10 ms apart, for example, a 1 ms pulse below would be a 10% duty cycle (1 ms/10 ms).
What is the frequency of this PWM signal?
Calculate the % duty cycle during each period, and the average voltage this produces each time.
What duty cycle would be needed to create the following average voltages? 1.2 V, 3.5 V, 4.8 V
This controller has 8-bit resolution (0 to 255). What is the resolution of the PWM output, in volts?
11

## Slide 12: What is pulse width modulation?
The frequency of the PWM signal is 100 Hz (1/10 ms = 100)
Duty cycles:
1.2 V: 24%, or 2.4 ms (1.2 V/5 V x 100% = 24%)
3.5 V: 70%, or 7 ms
4.8 V: 96%, or 9.6 ms
The resolution of the PWM output is 5 Volts / 256 steps = 0.02 V to 2 decimal places.
What is happening if the duty cycle is set to zero or 100%?
More generally, what is happening if the duty cycle stays the same?
How could PWM control the speed of a motor?
12

## Slide 13: Applying pulse width modulation: RGB LEDs
A CNC machine status light can be red, amber or green.
A microcontroller changes the status of the red, green or blue emitters in an RGB LED.
Each emitter can be on, dimmed (50% duty cycle) or off.
13
4. Pulse width modulation
First, think about what PWM signal to each emitter will create a red, yellow or green light. Then, consider whether you need to send a 50% duty cycle signal to the red or green emitter, while leaving the other on 100%, to change yellow to amber. Sketch on the activity sheet what PWM signals would make the light cycle through red, amber and green statuses.

## Slide 14: Applying pulse width modulation: DC motors
The CNC tool head motor has an operating speed of 0 to 12,000 rpm.
The microcontroller will operate a higher power PWM circuit to control the motor speed.
This PWM circuit will operate at a frequency of 50 kHz.
Complete the table on the activity sheet to show the duty cycles for a range of tool head motor speeds.
14
4. Pulse width modulation

## Slide 15: Applying pulse width modulation: servo motors
The tool head is controlled by a servo motor that can move from 0 to 180, with a resting position of 90.
The PWM signal for the servo has a frequency of 100 Hz.
The pulse width for the three key positions is 1 ms (0), 1.5 ms (90) and 2 ms (180).
Calculate the pulse width for the intermediate positions listed on the activity sheet.
If the microcontroller has an 8-bit (256 step) resolution, what is in principle the smallest increment by which the servo motor can rotate?
15
4. Pulse width modulation
Image © This Is Engineering

## Slide 16: Answers
9c. Servo motor
Angle Pulse width
ms (4dp)
9b. Tool head motor
rpm % (2dp) ms (4dp)
9a. LEDs
1.056
1.083
1.222
1.611
1.917
Speed Duty cycle Pulse width
8.33
16.66
41.67
66.67
91.67
1000
2000
5000
8000
11000
0.0017
0.0033
0.0083
0.0133
0.0183
The maximum theoretical resolution is 90/128 = 0.7 degrees
10
15
40
110
165
16
4. Pulse width modulation
Example:
(1000/12000) x 100% = 8.33% duty cycle.
(1/50000) x 8.33% = 0.0000017 s = 0.0017 ms
Example:
(10/180) x 1 = 0.056
0.056 + 1 = 1.056 ms

## Slide 17: Pulse width modulation at work
Power engineer
PWM saves energy compared with using transformers to regulate voltage.
Buildings engineer
PWM controls the brightness of my smart lighting system.
Automation engineer
PWM is used in the signals from the Internet of Things (IoT) devices that monitor our automated factory.
Robotics engineer
PWM signals control the speed and angle of my 6-axis robot arms.
Maintenance engineer
PWM manages the cooling fans on our CNC machines.
Safety engineer
PWM helps to control the drones I use to inspect our sites.
Where might you come across PWM control in a work environment?
You’ve explored how PWM allows microcontrollers to control a variety of output devices.
17
4. Pulse width modulation