## Slide 1
Microcontroller systems 1. Mechatronic systems and control

## Slide 2
2
Practitioner guide 1. Mechatronic systems and control

## Slide 3: Introduction and overview
These resources help practitioners to deliver the microcontroller systems components of engineering and manufacturing-related qualifications at levels 2 and 3. They introduce the topic and stimulate learners to explore and reflect on key concepts and are designed to complement and enhance practitioners’ own lesson materials and schemes of work.
Resources summary
The Level 3 resources develop learners’ understanding of sensors and actuators before using a series of realistic but simple scenarios to provide an introduction to PLCs and PLC programming. We suggest that practitioners adapt the activities to suit the range of sensors, actuators and PLCs available in their place of learning and to activities which relate to learners’ industrial placements. Practical extension suggestions enable learners to practise PLC programming using their preferred tool, software or simulator and to build a complete demonstration system.
Resource name | Level | PPT slides + notes - practitioner | PPT slides - learner | Activity sheets | Film | Interactive
1. Mechatronic systems and control | 2 |  |  | 3 |  | Optional
Delivery
Delivery suggestions for practitioners, and suggested answers where appropriate, are in the presenter’s notes for each slide. The core activities in each resource provide around 60 mins learning time, though additional suggestions, including independent learning, can extend this time significantly.
Overarching theme/big questions
What is a mechatronics/automated system?
What is the role of programmable logic controllers (PLCs) in mechatronics?
Overview
The Level 2 resource provides a bridge between Level 2 and Level 3. It helps learners to understand the purpose and features of a mechatronic system, identify examples of mechatronic systems in a range of settings, describe in simple terms how the different components in a mechatronic system work together to control a process, and identify some differences between a microcontroller, PLC and microcomputer, suggesting suitable applications for each.
1. Mechatronic systems and control | Practitioner guide
3

## Slide 4: Learning outcomes and resource links
Level 2 resource
Mechatronic systems and control
Name some examples of mechatronic systems in domestic and industrial settings.
List the main parts of a control system and describe how they work together.
Explain some differences between a microcontroller, a PLC and a microcomputer.
Full resource list available for the topic of
Microcontroller systems:
1. Mechatronic systems and control (Level 2)
2. Sensors and signals (Level 3)
3. Understanding control processes (Level 3)
4. Pulse width modulation (Level 3)
Links to other supported topics
CNC machinery, Electrical machines, Renewable energy, Robotics, Sustainability.
1. Mechatronic systems and control | Practitioner guide
4

## Slide 5: Subject coverage
Microcontrollers and PLCs
Mechatronics
Sensors and actuators in automation and control
Programmable Logic Controllers (PLCs)
Health and safety
Including careers
How different engineering sectors use control and automation
5
1. Mechatronic systems and control | Practitioner guide

## Slide 6: 1. Mechatronic systems and control
6

## Slide 7: Learning outcomes
You will be able to:
List the main parts of a control system and describe how they work together.
Explain some differences between a microcontroller, a programmable logic controller (PLC) and a microcomputer.
Name some examples of mechatronic systems in domestic and industrial settings.
7
1. Mechatronic systems and control
Image © This Is Engineering

## Slide 8
How does each example combine mechanical and electronic systems?
Use these examples to define a mechatronic system.
What is a mechatronic system?
In mechatronics, mechanical, electronic and control systems are combined to create a complete system. Mechatronic systems typically perform fast and precise motions and therefore require sophisticated electronic devices and control algorithms.
Dishwasher
Automatic doors
Printer
ATM
8
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
The Level 2 resources provide a bridge between Level 2 and Level 3. They help learners to understand the purpose and features of a control system in mechatronics, describe in simple terms how the different components in a control system work together to control a process, classify input and output devices, and identify some differences between a microcontroller, PLC and microcomputer. They also suggest examples of control systems in a range of industrial and other settings.
Starter activity
To introduce the concept of mechatronics systems and control, you may wish to:
Consider any simple mechatronic systems learners may have encountered on your site such as automatic doors, card entry systems, lifts or vending machines. What are they used for? What mechanical systems do they include? What electronics might control them?
Activity
Briefly review the examples on the slide (there is no need to get into the detail of how they function - just emphasise how they have something in common).
Ask learners to suggest where the two halves of the name come from. ‘Mecha’ from mechanical, and ‘tronic’ from electronic. (History: the term was invented and trademarked in 1971 by Yasawa Electric Corporation in Japan, who later released the rights to use the word.)
Ask learners to suggest a definition for mechatronics.
Example answers
Dishwasher: water pump, water heater, valves, control buttons and circuit board.
ATM: note counter and feed, card insertion and return, touch screen and computer.
Automatic door: motors, input from movement sensors and integration with building entry systems.
Printer: paper feed, printer head, input from computer.
Please also see the next slide.
Assessment
Verbal definitions.
Discussion and suggested examples of mechanical and electronic components.
Film
After completing this activity, learners can watch the Microcontroller systems film.

## Slide 9: Mechatronic systems and control
A mechatronic system combines electronics, mechanics and computer control to automate a process or response.
Sensor
Electronic controller
Input device
Output device
Identify the role of each part of a control system.
Arrange these parts and join them with arrows to show how an electronic system can control a mechanical system.
Add labels to show input, output and feedback.
9
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
You may wish to discuss bodily processes, such as sweating when it is hot, or picking up a can of drink. How does your body sense what is happening? What information does it need? How does it decide what to do? How does it respond? For example, bodies can respond to changes in internal temperature. When this rises over a certain amount, sweat glands open to release sweat which cools the body as it evaporates. Once the body senses that its temperature has fallen back to a ‘safe’ level, the sweat glands close.
Activity
Explain that every mechatronic system is made up of certain types of core components that work together in a consistent way, even though the exact components will vary depending on what the system is designed to do - hence any mechatronic system must include a control system.
Using the example below, discuss what each of the components on the slide does and how they might link to other parts of the system.
Use the following example: Ask learners to consider an electronic thermostat that controls a radiator valve.
The input device is the thermostat that sets the desired temperature of the room.
The sensor is a thermometer that measures the temperature of the room, to provide feedback as another input.
The controller compares the room temperature with the desired setting, to decide whether to open or close the radiator valve, and sends an output signal to the output device.
The output device is the solenoid (electrical relay) that opens or closes the valve.
Following your discussion, ask learners to turn their verbal ideas into a diagram of a mechatronic system by rearranging the boxes on the slide and using arrows to join them.
Activity sheet
Learners complete the diagram on Microcontroller systems - Activity sheet 1: section 1a, adding explanations of each part’s role and arrows to connect them.
Example answers
Please see the next slide.
Assessment
Discussion.
Diagrams.

## Slide 10: Mechatronic systems and control
Electronic controller
Provides the system with a goal
Compares the current state of the system with the goal to make decisions that reach the goal
Controls the mechanical system
Provides information about the state of the mechanical system or its environment
What do the arrows in the diagram represent?
What is the importance of feedback in a control system?
Output device
Sensor
Input
Output
Feedback
Input device
10
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
Activity
Review the diagram on the slide. Note that any system operates within its wider environment. Some systems may not need to sense this environment. For example, the motor controlling the speed of a conveyor belt may be controlled by a PLC that responds to a separate speed sensor elsewhere on the belt. In other applications, environmental sensing may be important, for example automated fire detection or CO sensing.
Discuss what the arrows on the diagram represent and the importance of feedback in a control system.
Activity sheet
Learners answer the questions on Microcontroller systems - Activity sheet 1: section 1b.
Example answers
The arrows represent the flow of information within the control system. This information flows as electrical signals.
Feedback happens when information about the state of a system and its environment are routed back to become inputs into the system. This enables the system to compare the current state with the desired state (from the input device). Without feedback, the system is unable to know what corrective action it needs to take in order to reach its goal. In the example of the radiator, the system would not know when to turn the radiator on and off in order to maintain the desired temperature.
Assessment
Discussion.
Written answers.
Interactive tool
Although principally intended for Level 3 learners, you may wish to let learners explore the Microcontroller systems interactive tool after completing this activity, which uses a room heating example. The diagram in the interactive tool is different to the above as it relates to how the process can be programmed, and so is an engineering drawing of a process control diagram. Please see the Level 3 resource 3. Understanding control processes in this Microcontroller systems module.

## Slide 11: Sensors and actuators
Sensors are input devices that provide information about the system’s goal or current state.
Actuators are output devices that change the state of the mechanical system.
Sort these examples into sensors and actuators.
Organise the sensors into their five categories as shown on the activity sheet.
Switch
Proximity switch
Lead screw
Gear train
AC motor
Stepper motor
Hydraulic piston
Tilt switch
Linear encoder
Flow rate
DC motor
Light beam
Rotary encoder
Pneumatic piston
Microswitch
Variable resistor
Thermistor
11
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
Learners can complete this activity individually or in pairs (either verbally or written).
Activity
Review the definitions of sensors and actuators.
Learners sort the examples on the slide into sensors and actuators.
Activity sheet
Learners organise each example onto Microcontroller systems - Activity sheet 2.
Example answers
Please see the next slide.
Assessment
Organisation into categories.

## Slide 12: Sensors
Hydraulic piston
Actuators
User input
Presence
Temperature
Light
Movement/ orientation
Switch
Variable resistor
Proximity switch
Microswitch
Light beam
Linear encoder
Tilt switch
Flow rate
Rotary encoder
AC motor
Thermistor
DC motor
Stepper motor
Pneumatic piston
Lead screw
Gear train
What output devices might a control system also include for the user?
What two types of information might a control system use to communicate with sensors and actuators?
Which of these types of information does the controller use to operate?
12
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
The questions on the slide can lead into a Level 3 discussion about signal processing and analogue-to-digital converters (ADCs).
Activity
Review the slide. You may need to explain that encoders convert the angular or linear position of an axle or slider into an analogue or digital signal.
Learners may note that there are many more sensors than actuator types, which fall into a small number of categories (although the mechanical systems they control will vary widely). Actuators may be electrical or mechanical devices that are electronically controlled. (Mechanical actuators can generally provide greater force.)
Use the questions on the slide to support a discussion of devices and information.
Example answers
Other output devices might include status or warning lights, LED displays to show operating parameters such as speed, or audible warning devices that provide information to the user.
Information will pass within the system as an analogue or digital electrical signal.
The controller is a digital device and will process digital information. This suggests that microcontroller systems need to include a way to convert analogue signals from some input devices into a digital signal the processor can understand - an analogue to digital converter, or ADC.
Assessment
Verbal suggestions and discussion.
Extension
Learners could research sensors and actuators, for example, by exploring an electromechanical component supplier’s website, and produce a report on the different categories available and their applications. This could support a discussion about what parameters an engineer should use to select the right sensor, such as input range, sensitivity and output signal.

## Slide 13: Microcontrollers, PLCs and microcomputers
Microcontroller
Dedicated computer on a chip
Embedded in a machine
Pre-programmed in factory
Multipurpose or single purpose
Usually low power
Dedicated input and output devices
Example:
Speed control on a brushless, cordless drill
Mechatronic systems use algorithms (rules or instructions) to process the inputs from setting controls and sensors and decide the outputs controlled by actuators. These algorithms are programmed into a microcontroller, programmable logic controller (PLC) or microcomputer.
Programmable Logic Controller (PLC)
Rugged, stand-alone device
Attached to a machine
Multipurpose, programmable
Usually higher power
Accepts a range of input and output devices that can be connected directly with no buffer or interface
Can be unitary (one) or modular (many)
Example:
Flow control in food manufacturing
Microcomputer
A general-purpose computer
Separate to a machine
Multipurpose, programmable using software
Accepts a range of input and output devices through an interface
Example:
Multi-axis robot control
13
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
If possible, have examples of dedicated IC microcontroller systems to hand. Highlight to learners that the microcontrollers they will learn to program at Level 3 (such as Arduino, PIC, PICAXE, Genie or ARM Cortex or STM32) are all microcontrollers that can be programmed using an external software IDE (integrated development environment).
Activity
Review this slide to help learners to complete the activity that follows.
Ask learners to identify how the types vary from the simplest (microcontrollers) to the most complex and adaptable (microcomputers).
Ask learners to explain how they think each type of controller is programmed.
Assessment
Discussion.
Verbal answers.

## Slide 14: Inputs, outputs and control
List at least one input and one output device that each system might contain.
What form of controller do they include?
What are the advantages of using this type of controller?
These systems all use dedicated microcontroller chips or PLCs.
Car automatic windscreen wipers
Pie filling machine
Smartphone
CNC milling machine
14
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
Learners could label a photo of each example. You may wish to include examples that more closely reflect learners’ planned industrial placements.
Activity
Briefly discuss each example on the slide and ask learners to identify the purpose of each system. (Smartphones have many purposes - can learners generalise this?)
Learners identify what sensors, actuators and controller each example may use, and why that type of controller provides advantages.
Activity sheet
Using Microcontroller systems - Activity sheet 3, learners complete the table with their ideas.
Example answers
Please see the next slide.
Assessment
Written answers.

## Slide 15: Inputs, outputs and control
These systems all use dedicated microcontroller chips or PLCs.
Input: Rain sensor
Output:
Wiper blade motor
Control:
Microcontroller
Input:
Weight sensor
Output:
Flow control valve
Control:
PLC
Input:
Screen (touch)
Voice
Motion
Output:
Audio
Haptic
Screen (visual)
Control:
Microcomputer
Advantages:
Small
Low power consumption
Powerful processor
Input:
Software program
Output:
Motion control motors
Tool motor
Control:
Microcomputer
Advantages:
Versatile
Easy to load new program
Car automatic windscreen wipers
Pie filling machine
Smartphone
CNC milling machine
Advantages:
Small
Cheap
Advantages:
Rugged
Programmable
15
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
Activity
Discuss the example answers on the slide.
Help learners to recognise the advantages of discrete chips, PLCs and microcomputers:
  Discrete chips are small and often cheap, making them ideal to embed in consumer devices. At the top of their range, smartphone chips can provide immense computing power at low power consumption, making it possible for smartphones to function as mobile general-purpose computers.
  PLCs can be relatively easy to program by a trained engineer, for example, to enable a change in the manufacturing process. An important advantage for PLCs is that they are built for harsh industrial environments with their inputs and outputs being more electrically robust than the IO for a typical PC or micro controller.
  Microcomputers offer the greatest processing power and versatility. (It’s worth considering that the microprocessor in a smartphone will rival that in many microcomputers.)
Assessment
Additional discussion.

## Slide 16: Where might we find control systems?
Identify one example of a control system in each environment.
Suggest what inputs and outputs they might include.
List some benefits your examples of control systems deliver for their users.
Food production
Manufacturing
Renewable energy
Healthcare and hospitals
Transport
Buildings
16
1. Mechatronic systems and control
Notes: Practitioner delivery suggestions
Learners can work in pairs or groups to complete this activity. Each pair or group can focus on one setting or several. Alternatively, lay out a large sheet of paper on each table (or a laptop with an online sharing tool such as Google Jamboard). Learners rotate in groups between each table to add their ideas. The final group to visit each table can organise and present the ideas.
Activity
Remind learners that a mechatronic system combines electronics, mechanics and computer control to automate a process or response.
Learners discuss and generate ideas for what examples of mechatronics might be found in each setting. Focus learners by asking them to consider what control process may need to take place in these settings.
Learners can identify examples of where an automated system might provide or improve safety.
Where available, allow learners to use the internet to search for examples.
Example answers
Safety examples are in bold:
Food production: Can, bottle or pie filling would use a flow or mass sensor to control a valve, delivering accurate and consistent product fills. Also: conveyor belt control, safety guard locking, faulty product detection and removal (ingredients, unsealed cans or bottles).
Manufacturing: Safety guard locking or position limiting in CNC milling or drilling would use a microswitch or proximity sensor to control a relay or solid-state contactor to prevent movement motors from working, creating a safe working environment. Also: injection moulding, product filling, overheat sensing in 3D printing or injection moulding.
Renewable energy: Wind turbine blade pitch control would use a rotary sensor to control the direction of movement of the nacelle (the housing at the top of the turbine) for safety and optimum efficiency. Also: remote fault sensing and solar power tracking.
Healthcare and hospitals: Auto-inject drug delivery pumps would use a timer as input sensor for regular dosing, along with a flow or volume meter (or linear position sensor) to control dosage. This delivers regular, accurate dosages for patients, for example, 24-hour pain control. Also: respirators, automatic blood pressure measurement, movable hospital beds and surgical robots.
Transport: Cruise control or speed limiters use a rotary speed encoder attached to the wheels to sense speed and provide an output (via the engine management system) to the fuel and air inputs to the engine. As well as driver comfort this increases safety, for example, to limit speed in a section of roadworks. Also: collision detection, antilock brakes, stability control and power steering.
Airports: Baggage control and automated routing to gates use QR code sensors to read baggage labels and control mechanical actuators that open and close routing gates in the system of conveyors to direct each bag to the correct gate. This makes baggage handling faster and more efficient, reducing errors.
Buildings: Heating, cooling and ventilation will use temperature sensors and other air quality monitors (perhaps humidity sensors and air flow sensors) to control the heating and fans that move cool or warm air in the building, maximising comfort while minimising energy use and losses. Also: pass-card security locks, lifts and electronic door locks.
Assessment
Discussion, examples and optional research.
Work experience/industry placement
Practitioners may wish to adapt this activity to include settings or industrial sectors in which learners will complete their industrial placements or work experience. Depending on scheduling, learners could write a brief report or presentation, with photos, of examples of mechatronic or control systems in their placement setting.

## Slide 17: Learning outcomes
You will be able to:
List the main parts of a control system and describe how they work together.
Explain some differences between a microcontroller, a programmable logic controller (PLC) and a microcomputer.
Name some examples of mechatronic systems in domestic and industrial settings.
17
1. Mechatronic systems and control
Image © This Is Engineering