## Slide 1
Battery technologies 1. Introducing battery technologies

## Slide 2: 1. Introducing battery technologies
2

## Slide 3: Learning outcomes
You will be able to:
List some criteria an engineer might consider when selecting a battery.
Make calculations of battery capacity in Watt-hours (Wh).
3
Identify challenges needed to create a circular economy for rechargeable battery packs.
1. Introducing battery technologies

## Slide 4: Batteries provide essential power
Batteries are a source of electric power.
4
1. Introducing battery technologies
List some industrial and domestic uses for batteries.
Use your understanding of the definition of power to explain what unit is used to describe a battery’s storage capacity.
Suggest some criteria an engineer might consider when selecting a battery.

## Slide 5: Key battery specifications
When choosing a battery, an engineer needs to consider a range of criteria including the battery’s:
voltage
storage capacity
dimensions
weight (mass)
discharge rate.
5
5
Suggest which criteria are most important for these four engineering applications.
Can you also prioritise your criteria?
I need a battery for an autonomous guided warehouse vehicle.
I need a battery for a new earbud design.
I need a battery for an electric delivery vehicle.
I need a battery for a handheld CNC controller.
1. Introducing battery technologies
Image © This Is Engineering
Application 1
Application 3
Application 2
Application 4

## Slide 6: Prioritising criteria for different applications
6
1. Autonomous guided vehicle (AGV)
Voltage – match to motor
Dimensions – minimise volume
Capacity – maximise time between charges
What two units can be used to specify battery capacity?
What is the relationship between these two ways to measure capacity?
3. Earbud
Dimensions – fit into a tiny body
Capacity – maximise listening time
Weight – earbuds need to be light
2. Electric vehicle (EV)
Dimensions – fit into vehicle design
Capacity – maximise range
Discharge rate – maximise power
4. Controller
Voltage – match to electronics
Dimensions – fit standard battery compartment
Capacity – maximise operational time
1. Introducing battery technologies

## Slide 7: Energy storage capacity
7
Battery storage capacities can be given as Amp-hours (Ah) or Watt-hours (Wh).
To convert from Ah to Wh you also need the battery voltage,
eg for a typical AA: 1200 mAh x 1.5 V = 1.8 Wh
Exactly what does measuring capacity in Amp-hours or Watt-hours describe?
Suggest the advantage and disadvantage of each approach.
Complete the missing information in this table.
Use your answers to rank the batteries in order, from highest to lowest capacity.
 | Ah | V | Wh
Predicted UK grid storage in 2025 | 95 MAh | 230 V | 
Compact EV | 110 Ah | 360 V | 
Earbud (single) | 90 mAh | 3.7 V | 
Cordless drill | 4 Ah | 18 V | 
Smartphone | 3.2 Ah | 3.7 V | 
eBike | 8.5 Ah | 36 V | 
1. Introducing battery technologies

## Slide 8: Energy storage capacity – answers
8
Battery capacity depends on both the total energy needed and the rate at which this energy needs to be used.
Amp-hours: The amount of storage capacity in terms of current (flow of charge) the battery can sustain, ie the total charge within the battery.
Advantage: Ah is a helpful way to compare battery capacities of the same voltage.
Disadvantage: Ah does not indicate the total energy the battery can provide as it ignores voltage.
Watt-hours: The total energy a battery can store. Advantage: A more complete measure of energy capacity as Wh also takes the voltage into account.
Disadvantage: Stated Wh may not account for changes in the terminal voltage across the battery during use.
 | Ah | V | Wh | Order
Predicted UK grid storage in 2025 | 95 MAh | 230 V | 2.18 GWh | 1
Compact EV | 110 Ah | 360 V | 39.6 kWh | 2
Earbud (single) | 90 mAh | 3.7 V | 0.33 Wh | 6
Cordless drill | 4 Ah | 18 V | 72 Wh | 4
Smartphone | 3.2 Ah | 3.7 V | 11.84 Wh | 5
eBike | 8.5 Ah | 36 V | 306 Wh | 3
1. Introducing battery technologies

## Slide 9: How can we make batteries more sustainable?
9
The 6Rs of sustainability help us to identify how to make rechargeable batteries more sustainable:
What changes do we need to create a circular lifecycle for batteries?
Rethink – design for sustainability as well as for people. Reduce – cut down on the materials and energy used to make a product.
Refuse – don’t use materials if they are not needed or if they harm the environment.
Raw materials
1% recycling
99% waste
Production
~500 recharge cycles
1. Introducing battery technologies
Reuse – make something new using all or parts of a product. Repair – design products so they can be fixed when they break down. Recycle – reprocess a product’s materials to make new things.

## Slide 10: Case study: Acceleron Energy – making batteries better
10
Acceleron produces the world’s most sustainable lithium battery packs in a full circular economy approach.
Battery packs are serviceable, upgradable and recyclable. Each individual part can be removed for repair, replacement or upgrade, extending the life of the system.
Batteries that have been replaced can be repurposed or recycled. For example, many batteries that need to be removed from high-specification packs are repurposed to provide accessible, recyclable energy storage in the Caribbean and Kenya.
How does each of the 6Rs play a part in Acceleron’s sustainable battery technology?
Image © Acceleron
1. Introducing battery technologies

## Slide 11: A circular economy for batteries
11
Raw materials
Extraction
Disposal
Waste
Fewer raw materials – less extraction and processing of expensive, finite metals.
Production
Consumption
Recycle
Reuse
Repair
Remanufacture into same or different products.
Product life extended by reuse and repair.
Less waste and pollution.
Materials flow in a cycle that maximises their value.
Testing technology can isolate individual cells to remove and replace - not the whole pack.
Batteries can be reused in a cascade of less energy-intensive applications.
Batteries Control boards
Non-electronic components
Make modular and repairable – no battery soldering, can upgrade control electronics.
Non-recyclable or non-repairable components.
Simplify construction.
1. Introducing battery technologies
Rethink
Refuse
Reduce

## Slide 12: Battery technologies, engineering and the future
Batteries play an essential role in modern industry and will be central to a transition away from fossil fuels for energy and transport.
12
Image © This Is Engineering
What do you think are the most important challenges for engineers to overcome?
How do you think battery technologies will transform engineering occupations?
1. Introducing battery technologies

## Slide 13: Learning outcomes
You will be able to:
List some criteria an engineer might consider when selecting a battery.
Make calculations of battery capacity in Watt-hours (Wh).
13
Identify challenges needed to create a circular economy for rechargeable battery packs.
1. Introducing battery technologies