## Slide 1
Electrical machines
1. Introducing electric motors

## Slide 2
2
Electrical machines
1. Introducing electric motors

## Slide 3: Learning outcomes
You will be able to:
Suggest an appropriate motor to use for a range of applications based on its qualitative characteristics.
Image © This Is Engineering
3
1. Introducing electric motors
Describe the differences between the field and armature windings in series and shunt-wound DC motors.
Name some different types of direct current (DC) and alternating current (AC) motors.

## Slide 4: Electric motors around you
Think about where you might find electric motors at home and in an engineering workplace.
List some examples of what equipment or appliances these motors might power, or arrange your ideas as two concept maps (one for the home and one for an engineering workplace).
What type of electrical power supply are these motors most likely to be connected to?
4
1. Introducing electric motors
Image © This Is Engineering

## Slide 5: Electric motors around you – example answers
How else could you classify the different motors above?
Can you think of any other types of electric motor that you could add to your classification?
5
1. Introducing electric motors
At home
In the workplace
Electric bike
26 V DC battery
Game console fan
12 V DC
Washing machine
230 V AC
Microwave oven 230 V AC
Electric toothbrush
1.2 V DC battery
Cordless drill
18 V DC battery
CNC spindle
230 V AC
Water pump 230 V AC
Forklift
48 V DC battery
2 tonne hoist
3-phase 415 V AC
Each motor is connected to lower-voltage DC, mains AC or, in the workplace, a higher-voltage 3 phase AC supply:

## Slide 6: Classifying electric motors – DC and AC motors
Every electric motor uses electromagnetism to create torque (rotating force). Electric motors operate on a DC or AC supply. The way in which this current is supplied to the motor and how the current is used to create torque is different in different motors.
Describe how the differences in each type of motor’s connection(s) can help you to distinguish between them.
- Coils on rotor
- Magnets or coils around outside create a fixed magnetic field
- Brushes touching commutator rings supply current to rotor coils
- Magnets on rotor
- Coils on outside create a fixed magnetic field
- Coils on outside create a changing magnetic field
- The changing field induces a current in the rotor
- AC coils on outside create a changing magnetic field
- Slip rings connect a separate DC current to the rotor
Brushed
Brushless
Induction
Synchronous
Direct current (DC)
Alternating current (AC)
Permanent magnet
Coiled wire
Electrical connection
Axle
1. Introducing electric motors
6
AC
DC

## Slide 7: Commutators v slip rings – visual differences
The rotor coils in a brushed DC motor need to always experience a turning force in the same direction.
Commutators are split connectors on either side of the axle that reverse the current every half turn, to allow this.
Conductive brushes press on each commutator during each half of a rotation. A gap briefly interrupts the current to stop the rotor ‘sticking’ when the coils align with the magnetic field.
In a synchronous AC motor the magnetic field changes direction with the AC current through the field coils. The rotor coils need a constant DC current that always flows in the same direction.
Two slip rings (one is hidden behind the other in the diagram below) provide this constant connection, again with conductive brushes pressing against them. There is no gap in slip rings.
1. Introducing electric motors
7
Brush
Commutator
Gap
Field coils
Axle
Rotor coils
Magnets
Axle
Rotor coils
Brush
(another is hidden behind)
Slip ring
(another is hidden behind)

## Slide 8: Brushed DC motors – series, shunt and compound
Brushed DC motors can have stationary field coils around the outside instead of permanent magnets, to create the magnetic field (‘excitation’).
The coils wound around the rotor create the torque (rotating force). These are also called the armature coils.
The field coils can be wound in series with the armature coils, in parallel, or a combination:
1. Introducing electric motors
Series
Compound
Shunt
- Field coils are in series with the armature coil
- Few, thick coils
- The same current flows through the field and armature coils
- Field coils are in parallel with the armature coil
- Many, thin coils
- The current from the supply is split between the field and armature coils
Use your understanding of voltage and current in series and parallel circuits to suggest why series and shunt field coils need to use different types of coil winding.
8
+
-
- Many, thin parallel coils with few, thick series coils on top
- All of the current from the supply flows through the series field coils and then is split between the shunt field and armature coils
+
-
Armature
+
-
Shunt
field
Armature
Shunt field
Series field
Series field
Armature

## Slide 9: Voltage, current and resistance in DC motors
The current through the armature coils makes them turn in the magnetic field. This turning induces a voltage across the coils, called the back emf E. (emf = electromotive force.)
The back emf acts in the opposite direction to the input voltage V. This reduces the current flowing through the armature coils.
At the motor’s operating speed, enough current flows to overcome mechanical and electrical losses, and to power the mechanical output. This is a lower current than was needed to start the motor.
Engineers need to understand how the input voltage creates a current through the field and armature coils, and how this differs in series and shunt-wound DC motors:
1. Introducing electric motors
Examine the circuit diagrams again. Remember that the field (f) and armature (a) coils each have resistance R and a current I flowing through them.
Use V=IR to help you verify the formulas by discussing the formulas linking voltage, current and resistance.
9
+
-
+
-
Shunt field
Series-wound:
Shunt-wound:
V = E + IRa + IRf
V = E + IaRa
V = IfRf
E
Ra
Rf
I
If
Ia
Rf
Ra
E

## Slide 10: Key characteristics of AC and DC motors
DC |  |  |  | AC |  | 
Brushless | Series wound | Shunt wound | Compound wound | Synchronous | Induction 230 V Single phase | Induction 400 V 3 phase
High speed High torque Wide range of speed control | High starting torque Good for traction (motive force) applications | Lower starting torque Good for constant speed applications | Reasonable starting torque and speed regulation - midway between series and shunt | Constant speed as load varies Best for low speed applications | Simple, rugged Limited speed control | Simple, rugged Limited speed control High power capacity
The unique construction of each type of motor gives them different characteristics.
Discuss your ideas for applications when speed control might be more important than torque characteristics, and vice versa.
1. Introducing electric motors
10

## Slide 11: Choose the right type of motor
11
Power tool
A cordless power tool motor needs to provide a wide range of speed and torque.
Forklift
A warehouse forklift truck needs very high starting torque for moving and lifting loads. It runs on a 48 V DC battery.
HVAC fan (heating, ventilation, air conditioning)
The extraction fans in a workshop will operate in a narrow speed range.
Clock
A factory wall clock needs a low-speed motor that runs off mains electricity.
Hoist
A high-load hoist needs a motor with very high power output.
Conveyor
A conveyor in a food processing plant must move at a consistent speed.
Apply what you have learned about the characteristics of DC and AC motors to choose the best type of motor for each application.
Give a reason for your choice.
1. Introducing electric motors

## Slide 12: Choose the right type of motor – example answers
12
Power tool
Brushless DC
The motor will run from a DC battery and provide a wide range of speeds and torques.
Forklift
Series-wound brushed DC
The motor provides high torque and can run off the truck’s 48 V battery.
HVAC fan
230 V single phase AC
Simple and rugged.
Clock
230 V AC synchronous
Performs well at low speed.
Hoist
400 V 3 phase AC induction
Can provide very high output power.
Conveyor
Shunt-wound brushed DC
This maintains speed under varying loads.
Discuss what other considerations could help to minimise the energy needed to power electrical motor-driven systems.
1. Introducing electric motors

## Slide 13: When might you need to select or use the right motor?
13
What engineering or manufacturing environments might you visit for an industry placement or job?
Identify what motor applications make the activities in this environment possible.
Machine tools
Powered hand tools
Automation
Heating or cooling
Ventilation or extraction
Vehicles
1. Introducing electric motors

## Slide 14: Learning outcomes
You will be able to:
Suggest an appropriate motor to use for a range of applications based on its qualitative characteristics.
Image © This Is Engineering
14
1. Introducing electric motors
Describe the differences between the field and armature windings in series and shunt-wound DC motors.
Name some different types of direct current (DC) and alternating current (AC) motors.