## Slide 1
Microcontroller systems 1. Mechatronic systems and control

## Slide 2: 1. Mechatronic systems and control
2

## Slide 3: Learning outcomes
You will be able to:
List the main parts of a control system and describe how they work together.
Explain some differences between a microcontroller, a programmable logic controller (PLC) and a microcomputer.
Name some examples of mechatronic systems in domestic and industrial settings.
3
1. Mechatronic systems and control
Image © This Is Engineering

## Slide 4
How does each example combine mechanical and electronic systems?
Use these examples to define a mechatronic system.
What is a mechatronic system?
In mechatronics, mechanical, electronic and control systems are combined to create a complete system. Mechatronic systems typically perform fast and precise motions and therefore require sophisticated electronic devices and control algorithms.
Dishwasher
Automatic doors
Printer
ATM
4
1. Mechatronic systems and control

## Slide 5: Mechatronic systems and control
A mechatronic system combines electronics, mechanics and computer control to automate a process or response.
Sensor
Electronic controller
Input device
Output device
Identify the role of each part of a control system.
Arrange these parts and join them with arrows to show how an electronic system can control a mechanical system.
Add labels to show input, output and feedback.
5
1. Mechatronic systems and control

## Slide 6: Mechatronic systems and control
Electronic controller
Provides the system with a goal
Compares the current state of the system with the goal to make decisions that reach the goal
Controls the mechanical system
Provides information about the state of the mechanical system or its environment
What do the arrows in the diagram represent?
What is the importance of feedback in a control system?
Output device
Sensor
Input
Output
Feedback
Input device
6
1. Mechatronic systems and control

## Slide 7: Sensors and actuators
Sensors are input devices that provide information about the system’s goal or current state.
Actuators are output devices that change the state of the mechanical system.
Sort these examples into sensors and actuators.
Organise the sensors into their five categories as shown on the activity sheet.
Switch
Proximity switch
Lead screw
Gear train
AC motor
Stepper motor
Hydraulic piston
Tilt switch
Linear encoder
Flow rate
DC motor
Light beam
Rotary encoder
Pneumatic piston
Microswitch
Variable resistor
Thermistor
7
1. Mechatronic systems and control

## Slide 8: Sensors
Hydraulic piston
Actuators
User input
Presence
Temperature
Light
Movement/ orientation
Switch
Variable resistor
Proximity switch
Microswitch
Light beam
Linear encoder
Tilt switch
Flow rate
Rotary encoder
AC motor
Thermistor
DC motor
Stepper motor
Pneumatic piston
Lead screw
Gear train
What output devices might a control system also include for the user?
What two types of information might a control system use to communicate with sensors and actuators?
Which of these types of information does the controller use to operate?
8
1. Mechatronic systems and control

## Slide 9: Microcontrollers, PLCs and microcomputers
Microcontroller
Dedicated computer on a chip
Embedded in a machine
Pre-programmed in factory
Multipurpose or single purpose
Usually low power
Dedicated input and output devices
Example:
Speed control on a brushless, cordless drill
Mechatronic systems use algorithms (rules or instructions) to process the inputs from setting controls and sensors and decide the outputs controlled by actuators. These algorithms are programmed into a microcontroller, programmable logic controller (PLC) or microcomputer.
Programmable Logic Controller (PLC)
Rugged, stand-alone device
Attached to a machine
Multipurpose, programmable
Usually higher power
Accepts a range of input and output devices that can be connected directly with no buffer or interface
Can be unitary (one) or modular (many)
Example:
Flow control in food manufacturing
Microcomputer
A general-purpose computer
Separate to a machine
Multipurpose, programmable using software
Accepts a range of input and output devices through an interface
Example:
Multi-axis robot control
9
1. Mechatronic systems and control

## Slide 10: Inputs, outputs and control
List at least one input and one output device that each system might contain.
What form of controller do they include?
What are the advantages of using this type of controller?
These systems all use dedicated microcontroller chips or PLCs.
Car automatic windscreen wipers
Pie filling machine
Smartphone
CNC milling machine
10
1. Mechatronic systems and control

## Slide 11: Inputs, outputs and control
These systems all use dedicated microcontroller chips or PLCs.
Input: Rain sensor
Output:
Wiper blade motor
Control:
Microcontroller
Input:
Weight sensor
Output:
Flow control valve
Control:
PLC
Input:
Screen (touch)
Voice
Motion
Output:
Audio
Haptic
Screen (visual)
Control:
Microcomputer
Advantages:
Small
Low power consumption
Powerful processor
Input:
Software program
Output:
Motion control motors
Tool motor
Control:
Microcomputer
Advantages:
Versatile
Easy to load new program
Car automatic windscreen wipers
Pie filling machine
Smartphone
CNC milling machine
Advantages:
Small
Cheap
Advantages:
Rugged
Programmable
11
1. Mechatronic systems and control

## Slide 12: Where might we find control systems?
Identify one example of a control system in each environment.
Suggest what inputs and outputs they might include.
List some benefits your examples of control systems deliver for their users.
Food production
Manufacturing
Renewable energy
Healthcare and hospitals
Transport
Buildings
12
1. Mechatronic systems and control

## Slide 13: Learning outcomes
You will be able to:
List the main parts of a control system and describe how they work together.
Explain some differences between a microcontroller, a programmable logic controller (PLC) and a microcomputer.
Name some examples of mechatronic systems in domestic and industrial settings.
13
1. Mechatronic systems and control
Image © This Is Engineering