## Slide 1
Engineering
materials
2. Physical and mechanical properties of materials

## Slide 2: 2. Physical and mechanical properties of materials
2

## Slide 3: Learning outcomes
You will be able to:
Make calculations of battery capacity in Watt-hours (Wh).
Name and define a range of physical and mechanical properties.
Explain the meaning of physical and mechanical properties.
Consider how to work safely and avoid potential hazards when using and processing materials.
2. Physical and mechanical properties of materials
3
Image © This Is Engineering

## Slide 4: Classification of engineering materials
An engineering material is any material used in the construction or production of artificial structures and objects.
Dyneema composite fabric (DCF)
Glass-reinforced plastic (GRP)
ABS
Brass
Copper
Glass
Iron
7000 series aluminium
MDF
Nylon
Oak
Plywood
Polyurethane
Porcelain
Spruce
Steel
2. Physical and mechanical properties of materials
4
Carbon fibre reinforced polymer (CFRP)

## Slide 5: How can we classify these engineering materials?
Non-ferrous
Timber
Non-metals
Thermo- sets
Thermo- plastics
2. Physical and mechanical properties of materials
5
Iron
Steel
Polyurethane
Oak
Spruce
Copper
7000 series
aluminium
Brass
CFRP
DCF
GRP
MDF
Plywood
Glass
Porcelain
Nylon
ABS
Ceramics
Composites
Metals
Polymers
Alloys
Pure
Alloys
Pure
Ferrous

## Slide 6: Physical and mechanical properties
Any material combines physical and mechanical properties.
Physical properties describe qualities that can be measured about the material without deforming it.
Mechanical properties describe how the material resists deformation in response to an applied force.
Discuss and suggest some examples of physical properties and mechanical properties you may have heard of.
6
2. Physical and mechanical properties of materials

## Slide 7: Understanding material properties
The Engineering materials interactive tool will help you to name and define a range of material properties.
Use the tool to complete the definitions of the material properties on activity sheet 3.
7
2. Physical and mechanical properties of materials
Step 3: Choose the correct name for the property and click to see if you are correct.
Step 2: Read brief descriptions of the material property they need.
Step 1: Choose an engineer, who will describe an engineering scenario.

## Slide 8: Understanding material properties – answers
Boiling point | The temperature at which a material changes from a liquid to a gas.
Density | A material’s mass per unit of volume.
Electrical conductivity | How well a material allows an electric current to flow through it.
Hardenability | The depth to which a material is hardened after putting it through a heat treatment process.
Magnetic permeability | How easily a magnetic flux can pass through a material.
Melting point | The temperature at which a material changes from a solid to a liquid.
Permittivity | How much a material will electrically polarise when exposed to an electric field.
Specific heat capacity (SHC) | The amount of energy needed to raise one unit of mass by 1 oC.
Thermal conductivity | How well a material allows heat energy to transfer through it.
Thermal expansivity | A material’s tendency to expand in volume when exposed to heat.
Physical properties:
2. Physical and mechanical properties of materials
Brittleness | How easily a material will fracture without deformation when under stress.
Compressive strength | The pushing load a material can resist before failure.
Ductility | A material's ability to deform without breaking when pulled under tension.
Elasticity | How much a material can deform and then return to its original shape when under stress load.
Hardness | A material’s resistance to deformation due to indentation (a sharp force) or abrasion (rubbing).
Malleability | A material’s ability to deform without breaking when put under compression.
Plasticity | How easily a material will permanently deform when under load.
Shear strength | How well a material can withstand a sliding failure in the material in the direction of the force.
Tensile strength | The pulling load a material can withstand before breaking.
Torsional strength | The ability of a material to withstand a twisting load.
Mechanical properties:
8

## Slide 9: Material processing to create the desired properties
Engineers process materials to create or increase desirable properties:
High speed steel (HSS)
Stainless steel
High carbon steel
Medium carbon steel
Low carbon steel
Iron
Wrought iron
Cast iron
Cast
Low melting point
Hard, brittle
Pans, stoves
High melting point
Malleable, ductile
Decorative ironwork
Softer, lower strength, good to machine weld Car bodies, building frames
Corrosion resistance
Marine hardware
High tungsten
or molybdenum
Very hard but brittle Machine tools
Hard outer layer
Gears, bolts
Hardening
Blades, heavy plant
Ductile, softer
Wires
High chromium
Hardness at high temperature
Drill bits, tool heads
Control carbon content
Add more alloy materials
When other elements are added to a pure metal it becomes an alloy.
Hammer
2. Physical and mechanical properties of materials
Case hardening
Annealing
Quenching/
tempering
9

## Slide 10: Engineering materials, hazards and safety
Engineers process materials to modify their properties and to produce finished structures or components. They will use a range of machines, from CNC mills and lathes, to presses or furnaces, and may use chemical treatments for hardening and other surface treatments or oil/water quenching baths.
Processing methods, or the materials themselves, can present risks to personal safety. Where a risk cannot be eliminated or substituted, engineering controls and administrative controls work alongside personal protective equipment (PPE) to protect against risks:
Engineering controls are design solutions that isolate people from the hazard.
Administrative controls are training solutions that change how people work, to remove the hazard.
PPE provides a final barrier that protects people from any remaining hazard.
10
Think about what type of workplace you might or did enter for your industry placement or first job.
On your activity sheet, suggest what materials and equipment you might use or observe.
Suggest some general engineering controls and administrative controls that might remove risks from the materials you might work with and any other materials or chemicals you may need to use. How might your workplace or machines be designed and how might you be trained?
2. Physical and mechanical properties of materials

## Slide 11: Engineering materials, hazards and safety – answers
Engineering controls
Design to remove excessive noise, temperature or physical effort, or the use of toxic materials.
Isolation from toxic materials.
Enclosure of high-risk parts, machines or workstations.
Extraction of toxic chemicals or particles, along with ventilation using fresh air.
Automation of processes using toxic materials.
Administrative controls
Training in safe working practices and hazard awareness.
Monitoring of hazardous materials or processes.
Maintenance to ensure safe operation.
Process improvement to reduce risks.
Rotation and breaks to remove workers from environments.
Signage to highlight risks and promote safe behavior.
2. Physical and mechanical properties of materials
11
Materials might include ferrous metals and alloys like steel or stainless steel, or non-ferrous examples like aluminium and its alloys, bronze or brass; polymers, or composite materials.
Machines might include manual or CNC mills, drills, lathes or grinders, laser cutting, power and manual hand tools, or additive machines like 3D printers or laser sintering.

## Slide 12: Learning outcomes
You will be able to:
Make calculations of battery capacity in Watt-hours (Wh).
Name and define a range of physical and mechanical properties.
Explain the meaning of physical and mechanical properties.
Consider how to work safely and avoid potential hazards when using and processing materials.
2. Physical and mechanical properties of materials
12
Image © This Is Engineering